LS&S Item # 756228

Cobolt Speechmaster

Talking Color Detector

Thank you for purchasing your new talking color detector. Please take a few minutes to read these instructions in order to familiarize yourself with its features.

Format:  The detector is rectangular in shape with a 4- position slide switch on one of the long sides.   If you hold it in your right hand with the slide switch on the right under your thumb. With your left hand, you can feel that the front face of the item has a raised circular speaker grill and a battery compartment with a recessed clip below it.

On the bottom edge is a calibration press switch.  On the bottom edge of the back of the item is a small bulge indicating the earphone socket. At the end facing away from you is a detachable dual purpose cover. It protects the sensing mechanism while the device is being carried in a pocket or bag.  On the inside of the detachable cover is a white plastic surface used during calibration.

CALIBRATION:

For best results the unit should be calibrated regularly, preferably at the start of each session and especially whenever the temperature changes significantly. Start with the cover still in place on the front of the case and the unit switched off. Press and hold the calibration switch while pushing the slide switch to any of the 3 "ON" positions. Release the calibration switch and wait a few seconds for the device to "Beep" then start saying "WHITE". You can now unclip the cover from the front end of the case and use the detector.

OPERATION:

The 3 forward positions adjust the volume of the speech; the rear position turns the detector off.	If you prefer to use the earpiece, it should be plugged into the socket. Plugging in the earpiece will turn the speaker off.

To obtain the color of a surface the cover should be removed and clipped onto the opposite end of the case for safekeeping.  The cover can fit on the opposite end of the item even with the earpiece plugged into the socket.

The detector nozzle should be held flat against the surface to be checked and the color will then be spoken automatically. Please note that it is important that no

light enters the detector around the edge of the nozzle if an accurate reading is to be obtained. In practice, this just means taking care to hold the nozzle squarely against the surface. If the item continues to "Beep" without speaking a color, this usually indicates that light is entering around the edge of the nozzle.

The case has been shaped to make it as comfortable as possible to hold in several different ways.  Colors will be repeated continuously and it is recommended that you wait for the second reading after positioning the nozzle.

The item will also work as a light detector.	If it is held away from a surface it will beep in daylight or artificial light.

The detector can see colors in various combinations and shades. Their intensity is indicated by the words LIGHT, DARK, VERY LIGHT & VERY DARK. Low color saturation is indicated by the word GREY

MAINTENACE

It is recommended that the cover be kept fitted to the device at all times to protect both the detectors and the calibration device.	If this white surface gets discolored or damaged the readings will become inaccurate.

Take care not to allow anything to be pushed inside the nozzle to avoid damage to the sensors.

The device uses 1  9 Volt Alkaline battery held in a compartment found on the flat side of the item below the speaker grill. The cover clip can be felt in a recess. The clip should be pulled gently towards the back of the case to release the cover and allow it to hinge up.

If you have any additional questions, please contact:

LS&S, LLC

www.LSSproducts.com

LSSinfo@LSSproducts.com

1-800-468-4789